## Slide 1: Sound transmission and recording
Study aid for learning of Communications Acoustics
VIHIM 000
Prof. Fülöp Augusztinovicz
BME Dept. of Networked Systems and Sefvices
fulop@hit.bme.hu

## Slide 2: Radio transmitting systems

## Slide 3: Propagation of radio waves in the atmosphere
Heavily dependent on frequency, season and hour of the day

## Slide 4
FM pickup range around Budapest

## Slide 5: Radio bands
Name | Symbol | Frequency | Wavelength | Applications
 | ELF | 3–30 Hz | 10,000–100,000 km | Directly audible when converted to sound (above ~20 Hz), communication with submarines
 | SLF | 30–300 Hz | 1,000–10,000 km | Directly audible when converted to sound, AC power grids (50–60 Hz)
 | ULF | 300–3000 Hz | 100–1,000 km | Directly audible when converted to sound, communication with mines
 | VLF | 3–30 kHz | 10–100 km | Directly audible when converted to sound (below ~20 kHz; or ultrasound otherwise)
 | LF | 30–300 kHz | 1–10 km | AM broadcasting, navigational beacons, lowFER, amateur radio
 | MF | 300–3000 kHz | 100–1000 m | Navigational beacons, AM broadcasting, amateur radio, maritime and aviation communication
 | HF | 3–30 MHz | 10–100 m | Shortwave, amateur radio, citizens' band radio, skywave propagation
 | VHF | 30–300 MHz | 1–10 m | FM broadcasting, amateur radio, broadcast television, aviation, GPR, MRI
 | UHF | 300–3000 MHz | 10–100 cm | Broadcast television, amateur radio, mobile telephones, cordless telephones, wireless networking, remote keyless entry for automobiles, microwave ovens, GPR
 | SHF | 3–30 GHz | 1–10 cm | Wireless networking, satellite links, amateur radio, microwave links, satellite television, door openers
 | EHF | 30–300 GHz | 1–10 mm | Microwave data links, radio astronomy, amateur radio, remote sensing, advanced weapons systems, advanced security scanning

## Slide 6: Radio systems
AM
  In MW band,
    Frequencies allocated in 9 kHz distance (E) or 10 kHz (US)
    Dynamic range 50 dB, bandwidth: 100-4500 Hz
  Amateur, large distance telecommunication etc.
FM
  In VHF band (CCIR), frequencies allocated in 100 kHz distance
    larger dynamics: 70 dB
    wider frequency range: 40-15000 Hz
Digital
  DRM (Digital Radio Mondiale)
  DAB, DAB+ (Digital Audio Broadcasting)
  DVB-T, DVB-S (Digital Video Broadcasting – Terrestrial/Satellite)

## Slide 7: Ranges of wavelength
1 cm
10 cm
1 m
10 m
100 m
1 km
mobil
~ 1:3
Tv (terrestrial)
~ 1:16
Radio
1:200
Sound
1:1000
30 GHz
30 MHz
300 MHz
3 GHz
300 kHz
3 MHz
FM
AM
digital

## Slide 8: Frequency bandwidth
AM, medium wave 100 - 4500 Hz
FM, VHF 40 - 15 000 Hz
TV: 40 - 15 000 Hz
Traditional records 30-10000 (but in new doncitions only) (LP, „bakelyte”): (harmonics up to 30 000 Hz)
MC (music cassette): 5 000-10 000 Hz
CD (compact disc): 20-18 000 Hz
SACD (=Super Audio CD): 20-200 000 Hz

## Slide 9: Dynamic range
AM, MW: 40-50 dB
FM 60-70 dB
Tv: the same as FM
Record: 30 - 40 dB
MC: 30 – 40 dB
CD: 96 dB
SACD: 110 dB
Ratio of the maximum and minimum transmittable signal components, in dB
Upper limit: distortion, lower limit: background noise

## Slide 10: Kivezérlés, hangosság, telítés, torzítás, fájlhiba…
Ez mind együtt:
The Loudness War
http://www.youtube.com/watch?v=3Gmex_4hreQ

## Slide 11: Outset of the stereo transmission
The first stereo radio (1961)

## Slide 12: The first virtual audio equipment
The phonograph of Th.A. Edison
(patent from 1877)
The telediffusion (on the phone) by T. Puskás, the first coverage from the Paris Opera House (1881)

## Slide 13: Phonograph cylinder

## Slide 14: Development of sound recording technologies
Mechanical record (Berliner, 1895)

## Slide 15: Purely electronic record player
45 rpm player (RCA, ~1948)

## Slide 16: Modes of operation

## Slide 17: Two channel (stereophonic) LP record

## Slide 18: Multichannel recording

## Slide 19: Development of stereo recording
One of the best: Sergeant Pepper’s Lonely Hearts’ Club (1967, Abbey Road Studio, George Martin, EMI Records)
„A defining album in the emerging psychedelic rock style, Sgt. Pepper was critically acclaimed upon release and won four Grammy awards in 1968. Acclaimed by critics and publications as one of the most important albums in the history of popular music.”

## Slide 20: The pickup

## Slide 21: Frequency correctio n
Record Industry Association of America - RIAA korrektor

## Slide 22: Tape recorder

## Slide 23: Studio tape recorder
Analogue multichannel recorder, e.g. a Studer A800 MK III.

## Slide 24: Typical equipment of today
Digital
Amatőr: pl. Zoom H4n, professzionális: Marantz PMD 661)