## Slide 1: Basic nositons of hearing and psychoacousics
Educational guide for the subject Communication Acoustics
VIHIAV 035
Fülöp Augusztinovicz
Dept. of Networked Systems and Services
fulop@hit.bme.hu

## Slide 2: Psychoacoustic phenomena
Sensing thresholds
Masking
  in time
  in frequency
Pitch [bark]
Cricital bands
Loudness [phon]
Sharpness [acum]
Fluctuation [vacil]
Roughness [asper]
Annoyance
Binaural hearing
  lateralization (1D)
  localisation (3D)

## Slide 3: The inner ear
Construction of the inner ear
A Corti-féle szerv
A csiga

## Slide 4: Relationship of the inner ear and the brain/ 1
Time domain decoding, speech processing
Spatial domain decoding, spectral processing (music)

## Slide 5
loudness
pitch
tone
sensed duration
sensed direction
etc.
Physical parameters
Perception parameters
intensity
frequency
spectrum
duration
direction
etc.
Φ
sensing organ
neural conduction
brain operation
Ψ
Relationship of the inner ear and the brain/2

## Slide 6: Sensing of direction by two ears
Basis of direction sensing: the two ears hear different sounds, both in amplitude and in phase
Description of the different hearing by the two ears is expressed by the HRTFs (Head Related Transfer Function)

## Slide 7: The measurement of HRTF

## Slide 8: The binaural hearing
Time-delay panning
Amplitude-panning
HRTF-filtering

## Slide 9: Use of binaural hearing for virtual (acoustic) reality
Time delay
Amplitude rendering
Head Related Transfer Function (HRTF) technique

## Slide 10: Virtual acoustics

## Slide 11: Masking of narrow-band noise
Hearing threshold shift for narrow band sounds of critical bandwidth, as a function of frequency and level.
Conclusions:
masking is stronger for higher frequencies
asimmetry is increased for higher intensities

## Slide 12: Masking for sinusoidal sounds: critical bands
Masking in the frequency domain
  the cochlea creates an "auditory filter„
  Characterized by critical bands:
    the band of audio frequencies within which a second tone will interfere with the perception of a first tone
    the band within which increasing the bandwidth of narrow band excitation will not increase the percepted loudness
Reason: geometry and characterictics of the basilar membrane

## Slide 13: Critical bandwidth vs. center frequency
Demo: increasing the bandwidth with constant energy
http://www.feilding.net/sfuad/musi3012-01/demos/audio/103_critical_bands_loudness.htm

## Slide 14: Critical bands
Each critical bandwidth corresponds to constant, 1,3 mm along the basilar membrane
but
Each critical bandwidth corresponds to varying frequency bandwidth

## Slide 15: Critical bands
Critical Band | Frequency (Hz) |  |  | Critical Band | Frequency (Hz) |  | 
 | Low | High | Width |  | Low | High | Width
0 | 0 | 100 | 100 | 13 | 2000 | 2320 | 320
1 | 100 | 200 | 100 | 14 | 2320 | 2700 | 380
2 | 200 | 300 | 100 | 15 | 2700 | 3150 | 450
3 | 300 | 400 | 100 | 16 | 3150 | 3700 | 550
4 | 400 | 510 | 110 | 17 | 3700 | 4400 | 700
5 | 510 | 630 | 120 | 18 | 4400 | 5300 | 900
6 | 630 | 770 | 140 | 19 | 5300 | 6400 | 1100
7 | 770 | 920 | 150 | 20 | 6400 | 7700 | 1300
8 | 920 | 1080 | 160 | 21 | 7700 | 9500 | 1800
9 | 1080 | 1270 | 190 | 22 | 9500 | 12000 | 2500
10 | 1270 | 1480 | 210 | 23 | 12000 | 15500 | 3500
11 | 1480 | 1720 | 240 | 24 | 15500 | 22050 | 6550
12 | 1720 | 2000 | 280 |  |  |  | 

## Slide 16: Standard octave and third-octave bands

## Slide 17: Loudness
Subjective loudness of a 1000 Hz sinusoidal sound equals the physical quantity: sound pressure level.

## Slide 18: Simulation of loudness by weighting functions
Historical development: inverse curves of the 40, 70 and 100 phon loudness curves (1928)
Very easy to implement by simple RC circuits
Obviously very rough approximation, still not yet obsolete
  A is generally used nowadays
  B, C has nearly died out
  D is used for jet aircrafts

## Slide 19: Summation of loudness /1
What happens, if sounds of various frequencies are summed?
  1 pc 1000 Hz 60 dBSPL sinusoidal sound  60 phon
  10 pc of 60 dBSPL sounds of various frequencies 
    Physically summed: 70 dB
    Loudnesses summed: 90 phon!
Why?

## Slide 20: Summation of loudness /2
Summation is different for slosely spaced and for faraway frequencies

## Slide 21: Summation of loudness
Tool for the summation: the Zwicker method

## Slide 22: Masking in time
Consequence: a new sound arriving with short time delay is not sensed as a separate sound but appears as the original sound would be stronger (Haas-effect)

## Slide 23: Implications and applications
Room acoustics
Optimization of digital sound processing (bit rate reduction, data reduction)
  Mp3 player
  Mobile phone technologies