## Slide 1: The speech
Study aid for learning of Communications Acoustics
VIHIM 000
Prof. Fülöp Augusztinovicz
BME Dept. of Networked Systems and Sefvices
fulop@hit.bme.hu

## Slide 2: Introduction
The language:
  Communication between the individuals of the human society
  Main tool of the human thinking
The speech:
  Primary manifestitation of the language
  Most widespread form of human communication (but by far not the only one)
  The very first, from the chronological point of view: well before writing

## Slide 3: Suggested literature
E. Keller (Ed.), Fundamentals of speech synthesis and speech recognition. Basic concepts, state-of-the-art and furure challenges. John Wiley, 1994.
P. Ladefoged & I. Maddieson: The sounds of the world’s languages Blackwell Publishers, 1985

## Slide 4: The natural chain of speech
Brain level
Brain level
Organic level
Organic level
Acoustical level
brain
speaking organ
brain
hearing organ
hearing organ
speaking organ

## Slide 5: The structure of speech
Sentence > word > syllable > phonema > speech sound
  Notion of phonemae:
  The smallest contrastive linguistic unit which may bring about a change of meaning

## Slide 6: The speaking organ / 1
Vocal cords
tongue
trachea
epiglottis
Nasal cavity
Soft palate
larynx
teeth
lips
Hard palate
Oral cavity
esophagus
linguo-palatalport
velarport
pharynx
linguo-alveolarport
labialport
the vocal tract

## Slide 7: The speaking organ / 2
Larynx and the vocal cords

## Slide 8: The speech production process / 1
release of air from the lung
the air at the larynx either
  passes through: unvoiced sound (consonants like s, t or f)
  Is set into vibration by the vocal cords: voiced (vowels or voiced consonants like m or z)
operation of ports (or valves)->production of various sounds:
  if velar port is open: nasal consonants or vowels (m, n, of franc)
  if linguo-palatal port is closed: k, g or ng
  in the linguo-alveolar port: mostly consonants e.g. explosives (t, d) and fricatives (s, z, ∫, ʒ)
  in labial port: p, b, t, v

## Slide 9: Example: articulation of voiceless plosives

## Slide 10: The speech production process / 2
The transmission system
  system of resonators (aka vocal tract, articulation channel)
Excitations
  voicing
  turbulence
  shock wave

## Slide 11: Excitation mechanisms
voice
turbulence
shock wave

## Slide 12: Classification of speech sounds
Vowels (V) i, é, ü, ö, e á, a, o, u
Consonants (C)
  stops
    nasals m, n, ny, ng
    plosives
    voiced b, d, g, gy
    voiceless p, t, k, ty
    rhotic / trill r
  lateral fricatives l, j
  fricatives
    voiced v, z, zs
    voiceless f, s, sz, h
  stop-fricatives (affricate)
    voiced dz, dzs
    voiceless c, cs

## Slide 13: The international phonetic alphabet

## Slide 14: Characteristics of vowels
FRF of the vocal tract
final spectrum, modified by the transmission of the vocal tract
line spectrum of the voice, female
line spectrum of the voice, male

## Slide 15: The oral cavity as a tuned resonator

## Slide 16: Formants of vowels

## Slide 17: Characteristics of consonants
Fricatives
  turbulent excitation > resonance of the vocal tract
Plosives
  cannot be held for long time
  no structure of formants
  shock wave > time out of vocal cords > stabilised vowel

## Slide 18: Articulation places of consonants

## Slide 19: Daabase of Hungarian speech sounds
http://magyarbeszed.tmit.bme.hu/index.php?p=interaktiv

## Slide 20: The speech intelligibility

## Slide 21: Influencing factors of intelligibility
  articulation capability of the speaker
  listening capability of the listener
  characteristics of the sound field (room acoustical parameters)
  level of background noise
Parameter 3 and 4 ae expressed in form of two ratios:
3. direct to reverberant ratio
and
4. signal to noise ratio

## Slide 22: Measurement of intelligibility
Subjective tests
  test with meaningless syllables
    invoking many test persons
    result is the ratio of correctly understood syllables to the total number of syllables, in %
  test with full sentences
Objecitve tests
  articulation index (AI): only background noise is considered
  Speech Intelligibility Index (SSI): reverberation is also taken into account
  Speech Transmission Index (STI): subjective quantity is approached by objective measurements (international standard)
    the speech consists of components of various frequencies, which are amplitude modulated by a low frequency envelope
    in order to remain intelligible, this modulation should be retained
    the transmission of this modulation without distortion is deteriorated both by multiple-path transmission (reverberation) and by background noise

## Slide 23: Effect of noise: Articulation index (AI)
Replacement rule of thumb: the signal to ratio should be as high as possible, but min. 5-10 dBA

## Slide 24: Effect of reverberation on the intelligibility
Original sound sample
In-situ recording
Measured impulse response
Artificially reverberated sound

## Slide 25: Calculation of STI
modulációs transzfer függvényen keresztül:
  mérése régebben kisfrekvenciásan modulált sávkorlátozott zajjal, újabban impulzusválasszal
ebből látszólagos jel-zaj értéket képezünk:
majd több lépés után:
wk 0.13 0.14 0.11 0.12 0.19 0.17 0.14

## Slide 26: Evaluation of STI values
Many figures of merit of intelligibility can be compared by using the CIS (Combined Intelligibility Scale) value:
CIS = 1 + lg (STI).

## Slide 27: Characteristics of the STI
It depends on
  signal to noise ratio
  reverberation
  bandwidth
  nonlinear distortions
  etc.

## Slide 28: Relationship of measurable SI descriptors
CIS
%